## Slide 1
PITCHATHON / REVIEW 1
AI-Based Solar Panel Performance Monitoring and Fault Detection
Review 1 — Problem, idea and feasibility
Signal Processing • Machine Learning • Analog Electronics
Team: ____________________ Guide: ____________________
KLH UNIVERSITY | PITCHATHON PROJECT
01

## Slide 2
PITCHATHON • REVIEW 1
Problem Statement & Need
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
02
• Solar output changes with sunlight, temperature, shading, dust and electrical faults.
• A panel can produce less power than expected without an obvious visible warning.
• Manual checking is periodic and may miss short-duration performance drops.
• We propose a low-cost monitoring prototype that flags suspicious readings and explains likely underperformance.
Goal: detect abnormal performance early — not replace certified protection systems.

## Slide 3
PITCHATHON • REVIEW 1
Project Objectives
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
03
Measure
Collect panel voltage, current and temperature; record irradiance if a sensor is available.
Estimate
Calculate power: P = V × I; compare measured output with an expected baseline.
Detect
Use rules first, then an ML model to classify normal vs. potentially abnormal behaviour.
Outputs: live readings • fault alert • timestamped CSV log • simple dashboard/console

## Slide 4
PITCHATHON • REVIEW 1
Proposed System Architecture
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
04
A layered design links analog measurement to digital analysis and alerts.
PV panel
DC output
Sensors + analog front end
Scale / filter
ESP32 / DAQ
Sample & transmit
Python pipeline
Features + ML
Dashboard / alert
Status + log
Prototype data can be simulated first; hardware integration follows after sensor calibration.

## Slide 5
PITCHATHON • REVIEW 1
Where Each Subject Fits
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
05
Analog Electronic Circuit Design
Voltage divider / conditioning, current sensing, low-pass filtering, ADC input protection.
Signal Processing
Sampling, noise filtering, moving averages, power calculation, trend and deviation features.
Machine Learning
Train a baseline classifier/anomaly detector from labelled or simulated sensor features.
Integrated ECE project: sensing → signal conditioning → feature extraction → decision.

## Slide 6
PITCHATHON • REVIEW 1
Feasibility & Execution Plan
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
06
• Stage 1: build a Python simulation and establish normal/abnormal patterns.
• Stage 2: connect ESP32 with calibrated voltage/current/temperature sensors.
• Stage 3: compare raw vs. filtered signals; calculate power and deviation from baseline.
• Stage 4: evaluate detection using held-out test data; tune thresholds and report limitations.
Minimum viable demo: Python model + CSV log + sensor/ESP32 plan.

## Slide 7
PITCHATHON • REVIEW 1
Expected Impact & Review-1 Deliverables
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
07
• Faster indication of underperformance and easier troubleshooting.
• Low-cost modular design suitable for a small panel demonstration.
• Visual evidence: normal vs. abnormal readings, power trend and fault labels.
• Deliverables now: block diagram, requirements, feasibility plan and initial software simulation.
Next review: show working data pipeline, initial model and test results.

## Slide 8
PITCHATHON • REVIEW 1
References & Safety Notes
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
08
• NREL — photovoltaic performance and operations resources: https://www.nrel.gov/solar/
• IEC 61724-1 — photovoltaic system performance monitoring (consult institutional access for the standard).
• ESP32 technical documentation: https://docs.espressif.com/
• Use isolated, low-voltage test setups; never connect a student prototype directly to mains or high-voltage PV strings.
• Any synthetic results must be clearly labelled as simulated; validate hardware readings before claims.