## Slide 1
PITCHATHON / REVIEW 2
AI-Based Solar Panel Performance Monitoring and Fault Detection
Review 2 — Design, algorithm and implementation
Signal Processing • Machine Learning • Analog Electronics
Team: ____________________ Guide: ____________________
KLH UNIVERSITY | PITCHATHON PROJECT
01

## Slide 2
PITCHATHON • REVIEW 2
System Design & Data Flow
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
02
Every sample is checked, cleaned and converted into meaningful indicators.
Acquire
V, I, T, irradiance*
Condition
Scale, filter, reject invalid
Features
Power, moving mean, deviation
Model
Rule threshold + ML
Report
Class, confidence, log
*Irradiance sensor is optional; without it, use a calibrated expected-power baseline.

## Slide 3
PITCHATHON • REVIEW 2
Signal Processing Pipeline
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
03
Sampling
Read sensors at a fixed interval and attach timestamps.
Filtering
Moving average reduces random noise while retaining slower changes.
Feature extraction
P = V × I; rolling mean; change from baseline; temperature-aware trend.
Important: use the same sampling interval and calibration for training and testing.

## Slide 4
PITCHATHON • REVIEW 2
Analog Front-End Plan
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
04
• Voltage: divider and suitable input protection scale panel voltage to ADC range.
• Current: Hall-effect or shunt-based sensor; select according to current range and isolation needs.
• Temperature: module or thermistor with calibrated conversion.
• Filtering: simple RC low-pass can reduce high-frequency noise; verify cutoff experimentally.
• ESP32 ADC readings require calibration; do not assume raw counts equal accurate volts.
Hardware values must be chosen from the actual panel and sensor datasheets.

## Slide 5
PITCHATHON • REVIEW 2
Machine Learning Approach
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
05
Baseline
Compare power against a normal reference adjusted for conditions when available.
Model
Random Forest classifier for normal / possible fault using voltage, current, temperature and derived features.
Validation
Train/test split; confusion matrix, precision, recall and false-alarm review.
Prototype labels are simulated unless real, verified fault-labelled measurements are collected.

## Slide 6
PITCHATHON • REVIEW 2
Fault Logic & Interpretation
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
06
• Low power: measured power remains well below the expected baseline for several samples.
• Sensor issue: impossible or stuck values, sudden discontinuity, or missing data.
• Thermal concern: temperature is unusually high alongside output decline.
• Shading / soiling / wiring issues can look similar; readings alone may not identify the exact physical cause.
Alert wording: “possible underperformance — inspect panel, shading, wiring and sensors.”

## Slide 7
PITCHATHON • REVIEW 2
Software Prototype & Demo Plan
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
07
• Python generates a reproducible sample dataset when no hardware CSV is supplied.
• Pandas/NumPy prepare features; scikit-learn trains and evaluates a classifier.
• The script saves a CSV log and a confusion-matrix image; optional input CSV supported.
• Demo: run script → inspect metrics → view sample alerts → explain how ESP32 data will replace simulated readings.
No fabricated hardware results: simulation is identified clearly in the output.

## Slide 8
PITCHATHON • REVIEW 2
Review-2 Tests & Risks
AI-BASED SOLAR PANEL PERFORMANCE MONITORING & FAULT DETECTION
08
• Test normal high-sunlight, low-light, hot-panel and abnormal-current scenarios.
• Compare raw and smoothed signals to show the effect of filtering.
• Check false positives caused by clouds or rapid irradiance changes.
• Risks: limited training data, sensor drift, calibration error, overlapping fault signatures.
• Mitigation: collect real data, add irradiance measurement, recalibrate and document limitations.